## Slide 1: OPENACC ONLINE COURSE
Lecture 2: GPU Programming with OpenACC
John Urbanic, Pittsburgh Supercomputing Center
October 26, 2017

## Slide 2: Course Syllabus:
October 19: Introduction to OpenACC
October 26: GPU Programming with OpenACC
November 2: Optimizing and Best Practices for OpenACC
Questions? Email openacc@nvidia.com

## Slide 3: Homework solution

## Slide 4: Exercise 1: C Solution
while ( dt > MAX_TEMP_ERROR && iteration <= max_iterations ) {
#pragma acc kernels
for(i = 1; i <= ROWS; i++) {
for(j = 1; j <= COLUMNS; j++) {
Temperature[i][j] = 0.25 * (Temperature_last[i+1][j] + Temperature_last[i-1][j] +
Temperature_last[i][j+1] + Temperature_last[i][j-1]);
}
}
dt = 0.0; // reset largest temperature change
#pragma acc kernels
{
for(i = 1; i <= ROWS; i++){
for(j = 1; j <= COLUMNS; j++){
dt = fmax( fabs(Temperature[i][j]-Temperature_last[i][j]), dt);
Temperature_last[i][j] = Temperature[i][j];
}
}
}
if((iteration % 100) == 0) {
track_progress(iteration);
}
iteration++;
}
Generate a parallel Kernel
Generate a parallel Kernel

## Slide 5: Exercise 1: Fortran Solution
do while ( dt > max_temp_error .and. iteration <= max_iterations)
!$acc kernels
do j=1,columns
do i=1,rows
temperature(i,j)=0.25*(temperature_last(i+1,j)+temperature_last(i-1,j)+ &
temperature_last(i,j+1)+temperature_last(i,j-1) )
enddo
enddo
!$acc end kernels
dt=0.0
!$acc kernels
do j=1,columns
do i=1,rows
dt = max( abs(temperature(i,j) - temperature_last(i,j)), dt )
temperature_last(i,j) = temperature(i,j)
enddo
enddo
!$acc end kernels
if( mod(iteration,100).eq.0 ) then
call track_progress(temperature, iteration)
endif
iteration = iteration+1
enddo
Generate a parallel Kernel
Generate a parallel Kernel

## Slide 6: CPU Performance
3372 steps to convergence

## Slide 7: Moving to the GPU
Change the target accelerator flag from “-ta=multicore” to “-ta=tesla”
% pgcc -acc -ta=tesla -Minfo=accel –DMAX_ITER=4000 laplace_kernels.c –o laplace.out
main:
65, Generating implicit copyin(Temperature_last[:][:])
Generating implicit copyout(Temperature[1:1000][1:1000])
66, Loop is parallelizable
67, Loop is parallelizable
Accelerator kernel generated
Generating Tesla code
66, #pragma acc loop gang, vector(4) /* blockIdx.y threadIdx.y */
67, #pragma acc loop gang, vector(32) /* blockIdx.x threadIdx.x */
76, Generating implicit copyin(Temperature[1:1000][1:1000])
Generating implicit copy(Temperature_last[1:1000][1:1000])
77, Loop is parallelizable
78, Loop is parallelizable
Accelerator kernel generated
Generating Tesla code
77, #pragma acc loop gang, vector(4) /* blockIdx.y threadIdx.y */
78, #pragma acc loop gang, vector(32) /* blockIdx.x threadIdx.x */
79, Generating implicit reduction(max:dt)

## Slide 8: Running on the GPU
  % ./laplace.out
  …
  ---------- Iteration number: 3100 ------------
  [995,995]: 97.58 [996,996]: 98.18 [997,997]: 98.71 [998,998]: 99.17 [999,999]: 99.55 [1000,1000]: 99.86
  ---------- Iteration number: 3200 ------------
  [995,995]: 97.62 [996,996]: 98.21 [997,997]: 98.73 [998,998]: 99.18 [999,999]: 99.56 [1000,1000]: 99.86
  ---------- Iteration number: 3300 ------------
  [995,995]: 97.66 [996,996]: 98.24 [997,997]: 98.75 [998,998]: 99.19 [999,999]: 99.56 [1000,1000]: 99.87
  Max error at iteration 3372 was 0.009995
  Total time was 40.462415 seconds.
Our time slows down by almost 7x from the original serial version of the code!

## Slide 9: What went wrong?
13.2 seconds copying data from host to device
% pgprof –cpu-profiling-mode top-down ./laplace.out
….
==455== Profiling result:
Time(%) Time Calls Avg Min Max Name
57.41% 13.2519s 13488 982.49us 959ns 1.3721ms [CUDA memcpy HtoD]
36.08% 8.32932s 10116 823.38us 2.6230us 1.5129ms [CUDA memcpy DtoH]
3.42% 788.42ms 3372 233.81us 231.79us 235.79us main_80_gpu
2.80% 646.58ms 3372 191.75us 189.69us 194.04us main_69_gpu
0.29% 66.916ms 3372 19.844us 19.519us 20.223us main_81_gpu_red
======== CPU profiling result (top down):
Time(%) Time Name
…
9.15% 16.3609s | __pgi_uacc_dataexitdone
9.11% 16.2809s | __pgi_uacc_dataonb
…
8.3 seconds copying data from device to host
Including the copy, there is an additional CPU overhead needed to create and delete the device data

## Slide 10: Architecture Basic Concept Simplified, but sadly true
High Capacity Memory
Shared Cache
High Bandwidth Memory
Shared Cache
$
$
$
$
$
$
$
$
$
$
$
$
$
$
$
$
$
$
$
$
PCIe Bus
GPU
CPU

## Slide 11: Multiple Times Each Iteration
CPU Memory
GPU Memory
CPU
GPU
A(i,j)
A(i+1,j)
A(i-1,j)
A(i,j-1)
A(i+1,j)
A(i,j)
A(i+1,j)
A(i-1,j)
A(i,j-1)
A(i+1,j)
A(i,j)
A(i+1,j)
A(i-1,j)
A(i,j-1)
A(i+1,j)
PCIe Bus
Excessive Data Transfers

## Slide 12: Excessive Data Transfers
while ( dt > MAX_TEMP_ERROR && iteration <= max_iterations ) {
#pragma acc kernels
for(i = 1; i <= ROWS; i++) {
for(j = 1; j <= COLUMNS; j++) {
Temperature[i][j] = 0.25 * (Temperature_old[i+1][j] + …
}
}
Temperature, Temperature_old resident on host
Temperature, Temperature_old resident on host
Temperature, Temperature_old resident on device
Temperature, Temperature_old resident on device
4 copies happen every iteration of the outer while loop!
#pragma acc kernels
for(i = 1; i <= ROWS; i++) {
for(j = 1; j <= COLUMNS; j++) {
Temperature[i][j] = 0.25 * (Temperature_old[i+1][j] + …
}
}
Temperature, Temperature_old resident on host
Temperature, Temperature_old resident on host
Temperature, Temperature_old resident on device
Temperature, Temperature_old resident on device
}
dt = 0.0;

## Slide 13: Data Management The First, Most Important, and Possibly Only OpenACC Optimization

## Slide 14: Data Construct Syntax and Scope
Fortran
!$acc data [clause …] structured block !$acc end data
C
#pragma acc data [clause …] {
structured block
}

## Slide 15: Data Clauses
copy( list ) Allocates memory on GPU and copies data from host to GPU when entering region and copies data to the host when exiting region.
Principal use: For many important data structures in your code, this is a logical default to input, modify and return the data.
copyin( list ) Allocates memory on GPU and copies data from host to GPU when entering region.
Principal use: Think of this like an array that you would use as just an input to a subroutine.
copyout( list ) Allocates memory on GPU and copies data to the host when exiting region.
Principal use: A result that isn’t overwriting the input data structure.
create( list ) Allocates memory on GPU but does not copy.
Principal use: Temporary arrays.

## Slide 16: Array Shaping
Compilers sometimes cannot determine the size of arrays, so we must specify explicitly using data clauses with an array “shape”. The compiler will let you know if you need to do this. Sometimes, you will want to for your own efficiency reasons.
C
#pragma acc data copyin(a[0:count]), copyout(b[s/4:3*s/4])
Fortran
!$acc data copyin(a(1:end)), copyout(b(s/4:3*s/4))
Fortran uses start:end and C uses start:count
Data clauses can be used on data, kernels or parallel

## Slide 17: Compiler will (increasingly) often make a good guess…
int main(int argc, char *argv[]) {
int i;
double A[2000], B[1000], C[1000];
#pragma acc kernels
for (i=0; i<1000; i++){
A[i] = 4 * i;
B[i] = B[i] + 2;
C[i] = A[i] + 2 * B[i];
}
}
pgcc -acc -Minfo=accel loops.c
main:
6, Generating implicit copy(B[:])
Generating implicit copyout(C[:])
Generating implicit copyout(A[:1000])
7, Loop is parallelizable
Accelerator kernel generated
Generating Tesla code
7, #pragma acc loop gang, vector(128)
C Code
Compiler Output
Smart
Smarter
Smartest

## Slide 18: Data Regions Have Real Consequences
  int main(int argc, char** argv){
  float A[1000];
  #pragma acc kernels
  for( int iter = 1; iter < 1000 ; iter++){
  A[iter] = 1.0;
  }
  A[10] = 2.0;
  printf("A[10] = %f", A[10]);
  }
Simplest Kernel
With Global Data Region
Output:
A[10] = 2.0
  int main(int argc, char** argv){
  float A[1000];
  #pragma acc kernels
  for( int iter = 1; iter < 1000 ; iter++){
  A[iter] = 1.0;
  }
  A[10] = 2.0;
  printf("A[10] = %f", A[10]);
  }
Output:
A[10] = 1.0
A[ ]
Copied
To GPU
A[ ]
Copied
To Host
Runs
On
Host
#pragma acc data copy(A)
{
}
A[ ]
Copied
To GPU
Still
Runs On
Host
A[ ]
Copied
To Host

## Slide 19: Data Regions vs. Compute Regions
  int main(int argc, char** argv){
  float A[1000];
  #pragma acc kernels
  for( int iter = 1; iter < 1000 ; iter++){
  A[iter] = 1.0;
  }
  A[10] = 2.0;
  printf("A[10] = %f", A[10]);
  }
Output:
A[10] = 1.0
#pragma acc data copy(A)
{
}
Data
Region
Compute
Region

## Slide 20: Data Movement Decisions
Much like loop data dependencies, sometime the compiler needs your human intelligence to make high-level decisions about data movement. Otherwise, it must remain conservative – sometimes at great cost.
You must think about when data truly needs to migrate, and see if that is better than the default.
Besides the scope-based data clauses, there are OpenACC options to let us manage data movement more intensely or asynchronously. We could manage the above behavior with the update construct:
C Fortran
#pragma acc update [self(), device(), …] !$acc update [self(), device(), …]
Ex: #pragma acc update self(Temp_array) //Get host a copy from device

## Slide 21: Analyzing / Profiling

## Slide 22: OpenACC Development Cycle
Analyze your code, and predict where potential parallelism can be uncovered. Use profiler to help understand what is happening in the code and were parallelism may exist
Parallelize your code, starting with the most time consuming parts. Focus on maintaining correct results from your program
Optimize your code, focusing on maximizing performance. Performance may not increase all-at-once during early parallelization
Analyze
Parallelize
Optimize
Analyze
Notes: This is the OpenACC development cycle. Analyze -> Parallelize -> Optimize. Rinse and repeat. It is slightly over-simplified, however. It is very important to profile you code before beginning, however, it is equally important to continue profiling your code as you make changes. It is important to verify that changes you are making are impacting the code in a way that you expected.
The Modules are designed to follow this format. This Module will include the Analyze portion. We are expecting students to profile for every module, however.

## Slide 23: Profiling gpu code
This is the view of PGPROF after profiling a GPU application
The first obvious difference when compared to our command line profile: a visual timeline of events
Using PGPROF to profile GPU code

## Slide 24: Profiling gpu code
Using PGPROF to profile GPU code
MemCpy(HtoD): This includes data transfers from the Host to the Device (CPU to GPU)
MemCpy(DtoH): These are data transfers from the Device to the Host (GPU to CPU)
Compute: These are our computational functions.

## Slide 25: Inspecting the PGPROF Timeline
Zooming in gives us a better view of the timeline. It looks like our program is spending a significant amount of time transferring data between the host and device. We also see that the compute regions are very small, with a lot of distance between them.
CPU overhead time including:
- Device data creation and deletion
- Virtual to Physical Host Memory Copy
Device Memory Transfers
Compute on the Device
* Note we use a 1 kernel solution (available from the Resources console)

## Slide 26: PROFILE after adding a data region
Pinned to Virtual Host memory copy
Update to host
Device compute
After adding a data region, we see lots of compute and data movement only when we update.

## Slide 27: Exercise 2 Use acc data to minimize transfers
Q: What speedup can you get with data + kernels directives?
Start with your Exercise 1 solution (or ours).
  Add data directives where it helps.
    Think: when should I move data between host and GPU? Think how you would do it by hand, then determine which data clauses will implement that plan.
    Hint: you may find it helpful to ignore the output at first and just concentrate on getting the solution to converge quickly (at 3372 steps). Then worry about updating the printout (hint, hint).

## Slide 28: Exercises: General Instructions
The exercise is found at https://nvlabs.qwiklab.com
  Create an account or log in (use the same email you registered for the course with)
  Open class: OpenACC Course Oct 2017

## Slide 29
TODAY WE DISCUSSED
Questions? Email openacc@nvidia.com
What OpenACC data directives are
Why they are important for GPU use
How to spot these, and many other types of performance hotspots, with a Profiler

## Slide 30: OPENACC Resources
Resources
https://www.openacc.org/resources
Success Stories https://www.openacc.org/success-stories
Events
https://www.openacc.org/events
Guides ● Talks ● Tutorials ● Videos ● Books ● Spec ● Code Samples ● Teaching Materials ● Events ● Success Stories ● Courses ● Slack ● Stack Overflow
Compilers and Tools https://www.openacc.org/tools
FREE
Compilers
https://www.openacc.org/community#slack

## Slide 31: OpenACC for Everyone
New PGI Community Edition Now Available
PROGRAMMING MODELS OpenACC, CUDA Fortran, OpenMP, C/C++/Fortran Compilers and Tools |  |  | 
PLATFORMS X86, OpenPOWER, NVIDIA GPU |  |  | 
UPDATES | 1-2 times a year | 6-9 times a year | 6-9 times a year
SUPPORT | User Forums | PGI Support | PGI Professional Services
LICENSE | Annual | Perpetual | Volume/Site
FREE
DOWNLOAD
https://www.pgroup.com/products/community.htm

## Slide 32: New Book: OpenACC for Programmers
Discover how OpenACC makes scalable parallel programming easier and more practical
Get productive with OpenACC code editors, compilers, debuggers, and performance analysis tools
Build your first real-world OpenACC programs
Overcome common performance, portability, and interoperability challenges
Efficiently distribute tasks across multiple processors
Edited by: By Sunita Chandrasekaran, Guido Juckeland
Use code OPENACC during checkout for 35% off
*Discount taken off list price. Offer only good at informit.com
READ MORE
http://www.informit.com/store/openacc-for-programmers-concepts-and-strategies-9780134694283

## Slide 33: XSEDE Monthly Workshop Series
NSF Funded for the national scientific community
Wide Area Classroom (WAC) Format
Next OpenACC event is November 7th
Classroom based with 25 remote sites per event
50 events, 8000 students and counting
Contact Tom Maiden, tmaiden@psc.edu

## Slide 34: Course Syllabus:
October 19: Introduction to OpenACC
October 26: GPU Programming with OpenACC
November 2: Optimizing and Best Practices for OpenACC
Questions? Email openacc@nvidia.com